## Slide 1: RT Telemetric (TLM) SW DR DR: 1.02
26.08.18

## Slide 2: RT TLM General Requirements
RTC shall record system status and events from RTC SW modules and export them to RT viewer using UDP connection.
The telemetric module will consist data base files (*.c, *,h) for each RTC module. This files will consist all the data members that need to be sample throw the telemetric procedure.
Each telemetric member will consist the following information fields:
  Module: the RTC module that the data member belong to (e.g. PFD, UAV, etc.…) [up to 32 groups].
  Data index: The member location at the telemetric RTC module structure [ up to 255 parameters in module].
  Offset [void*]: memory address of the data at the RTC module.
  Data type: Data type of the data [INT8, UINT8, INT16, UINT16, INT32, UINT32, INT64, UINT64 FLOAT_DOUBLE ].
  Visually: Indicate that the data will be show in RT viewer application (visually = true).
  Flash: Indicate that the data will be saved at Flash. (Flash = true).
  Group number: Indicate the rate sample in mSec (up to 10 possible groups) (Each group rate speed can configure throw “offline parameters”).
  CRC8 – Each data member will store CRC-8 for data traceability.
Each telemetric data member that will saved to Flash / Current structure will be saved at the following form:
  Data: The member data will be convert to bytes.
  Information bytes (3 bytes): This bytes consist the telemetric member information by bit fields at the following order:

## Slide 3: RT telemetric – high level module diagram
TLM
HKY
RTI
ETC.
RTC
Viewer
UDP
Registry
Registry
Registry

## Slide 4: RT TLM Flash – general requirements
RTC shall record system status and events using read / write to internal FLASH memory in the following conditions:
  Each telemetric data shell be belong to one of 10 possible programs. This program will contain all the telemetric members that belong to him.
  Each program (1 – 10 possible groups) will have Flash section (memory space) to store all the telemetric members that belong to this program.
  The Flash address limits for each program define once by calculation at a boot time process.
  The System Engineer will have the available memory space for each program on Flash. With this information the System Engineer shell supply the number of iterations for each program to save.
  Program header bytes: This header will be a part for each program section on the Flash. This header consist:
    Time stamp: Will indicate the latest write to Flash.
    Address of the last buffer to write to Flash.

## Slide 5: RT TLM Flash – Read / write requirements
  Flash write speed: each telemetric groups will manage local buffer to store all the telemetric members that belong to him. When the size of this buffer shell be:
  Flash write rate: This rate will indicate the time interval to store the entire programs contents to Flash. This time will be configurable throw the offline parameters.
  Write to Flash HBS API: the methods that will handle write to Flash shall be: p_CDS_write.
FLASH - Write
  Read from Flash: The RT viewer shall be read all programs contents upon user request from RT viewer. The user shall define to read contents from Flash by select this options throw RT Viewer
  The write to flash operations will be protected in thread safe (this protection will be a handle by HBS SW layer).
  Read from Flash HBS API: the methods that will handle read from Flash shall be: p_CDS_read.
FLASH - Read

## Slide 6: Telemetric SW flow Flash write process

## Slide 7: RT TLM Telemetric current state - requirements
RTC shall record current system data and present it in RT viewer upon user request and based on the following conditions:
  The local buffers that shall be use by the Flash mechanism shall be able to present via the RT viewer upon user selection on any given time. The user shall select this option on the RT viewer.
  Upon any given read the telemetric data the timestamp shall be read as well .

## Slide 8: RT TLM RT viewer requirements
The RT viewer shell present telemetric data from upon user request at any given time from 3 different sources:
  Current data: Current condition of the RTC telemetric members.
  Flash data: All Flash blocks that had been written to Flash (from latest to oldest).
  File: raw data that had been previous stored (format of text file).
The RT viewer shell present the telemetric data at the following way:
  Table of all members: This table will consist all telemetric members information one after one. This data can be view at:
    Sort values: The user will be able to sort those data from low to high, low to high or group them by RTC module.
    Data view: The user will be able to view members data by bytes or by original data values.
  Visual way: The user will able to search after data member by his name or index and by his group. Then the RT viewer shell present for this selected member a 2D figure and table of results by time stamp.
The RT viewer shall present telemetric members by his names:
  The telemetric members names will be read from generated file. This file generate by 3d application.
The RT viewer shall saved output files:
  Upon user request the RT viewer shell generate the following output files:
    Table of all members – At text file.
    Raw data of the incoming data.
    Picture (format *.jpg) of the 2D figure.

## Slide 9: RT TLM RT viewer - Presentation of table

## Slide 10: RT TLM RT viewer - Presentation of table

## Slide 11: RT TLM parameters configuration Solution A – ICD messages
Each telemetric plan will be in an ICD file format (.grep file).
The telemetric plan members will be build throw GDE application.
The ICD message will be form by system engineers.

## Slide 12: RT TLM parameters configuration Solution B – Parameters configurator tool
Parameters configurator tool goal is to add ability to insert / remove / view parameters for a chosen RTC module.
Configure path to DB files and module
Insert new parameter
Remove parameter from module DB
View module parameters

## Slide 13: RT TLM parameters configuration Solution B – Parameters configurator tool
The tool actually edit the implementation data base files for the selected module.
Create Telemetric object (in *.h file) with the given name (e.g. “TEST_FLAG”).
Create configuration function for the new parameter
Add the parameter function configuration
to module initialization procedure.
Update parameters module counter with amount of objects

## Slide 14: Telemetric SW flow Write process

## Slide 15: Telemetric SW flow Flash write task, initialize process

## Slide 16
The End.